## Slide 1
EN 50463 update Bart Van der Spiegel, Infrabel

## Slide 2: EN 50463: history
Started on request of European Commission and ERA in 2007.
First edition of EN 50463 series published in 2012.
TSI LOC&PAS and TSI ENE of 2014 referred to EN 50463:2012. EMS became mandatory on all new, renewed and upgraded trains.
An interface between two TSIs shall be uniquely defined.
A second edition of EN 50463 series was published in 2017. This version included a first protocol for the communication between the Energy Measurement System (EMS) on-board and a Data Collecting System (DCS) on ground.

## Slide 3: EN 50463: start of new Working Group 37
Nov 2023
& Jan 2025
18/7/2025
Feb 2026
Jul 2026
Dec 2026
Ad-hoc group revision EMS clauses in TSI
22/9/2025 > …
Apr 2025
Apr 2026
prEN 50463
FprEN 50463
Revision TSIs
Dec 2026
Input on how EN should be adjusted to fit new clauses of TSI
Draft for prEN 50463
FprEN 50463
Correct referencing possible
TSI LOC&PAS TSI ENE
Cybersecurity
With experts of EN 50463, ERA and ERJU
Translation
Translation
Translation
Enquiry
Enquiry
4/9/2025
31/10/2025
16/9/2025 > …
CCMC
QC
QC
EN 50463
Secretariat enquiry
HAS
HAS
HAS
HAS
3

## Slide 4
Distinction between Energy Measurement System and Consumption Point (i.e. EMS installed on-board)
Introducing multiple changes for hybrid trains
Clarifying process of commissioning and maintenance
Introducing possibility to have integrated energy measurement function combining current measurement, voltage measurement and energy calculation
Introduce secure protocols
Add possibility of a direct connection on-board
Add standardised digital signature, uncompressed payloads and mechanism for a batch of samplings at a higher frequence (e.g. every second)
The same protocol will be used in EN 50463 and IEC 62888; we are paving the road for a merged version in 203x
Main changes to EN 50463
4

## Slide 5: Timeline
1st November 2025: start of 3-month enquiry on prEN 50463 (CENELEC)
19th November 2025: webinar on prEN 50463 (Eress)
December 2025: publication of outcome of AS-03 (ERA)
January 2026: input from ERA to prEN 50463 (ERA)
December 2026: approval of EN 50463 (CENELEC)
December 2026: report with proposal of changes to TSI (ERA)
June 2027: approval by RISC of Commission Implementing Regulation (EC) adopting the changes to TSI
December 2027: possibly an Edition 2 on IRS 90930 (UIC)
5